OSLUV Lamp Build Instructions
# Printing Housing Parts
1. If you already have the 3D printed housing parts, skip this step.
2. The source files for the housing parts are in 3 separate files:
  1. housing.sldprt
  2. back_plate.sldprt
  3. emitter_ballast_spacer.sldprt
  4. shims.sldprt
  5. lens_cap.sldprt
3. Derived STEP files are also available:
  1. housing.step
  2. back_plate.step
  3. emitter_ballast_spacer.step
  4. shims.step
  5. lens_cap.step
# Housing Preparation
1. Remove all external burrs from 3D printed housing parts (black). Use a knife, chisel, and sandpaper as needed. Do not leave sharp edges.
2. Use a soldering iron to heat-press the M2.5 brass threaded inserts (4 per housing). Ensure they remain straight.
3. Slide the two 1/4”-20 threaded steel T-slot nuts into place.
4. Insert the two white plastic shims to prevent the T-slot nuts from falling out.
# Controller Preparation
1. Ensure resistors R1, R3, R5, and R6 are removed from the USHIO RP2040 Controller 1.0.
2. Unclip the fan wires from the fan housing, taking care not to stress the solder joint.
3. Cut the fan wires to a length of approximately 70mm.
4. Strip 8mm of insulation off the ends of the fan wires.
  1. Set the Knipex automatic stripper to “8mm”.
  2. Twist the strands together.
5. Tin the bare ends of the fan wires with solder.
6. Clean any flux off the tinned fan wires.
7. Insert the fan wires into the J3 connector.
  1. Match the red wire with “+”, and the black wire with “-”.
  2. Note: the wires are not removable. Please do not screw up.
# Controller Cable Preparation
1. Plug four 6” JST XA jumper wires into a 4-pin JST XA housing.
2. Connect the jumper wire in the pin 1 housing position to pin 1 of a second housing.
3. Continue connecting the remaining jumper wires to the second housing. Pin 2 to pin 2, pin 3 to pin 3, pin 4 to pin 4.
# High Voltage Cable Preparation
1. Cut two pieces of the white high-voltage silicone wire to a length of 80mm.
2. Strip 6mm of insulation off one end of each wire.
  1. Set the Knipex automatic stripper to “6mm”.
  2. Do NOT twist the strands together.
3. Crimp the M2.5 ring terminal on each wire, using the “22-14” slot.
4. Strip 3mm of insulation off the other end of each wire.
  1. Do NOT twist the strands together.
5. Crimp the JST VH terminal on each wire, uting the “20 AWG” slot.
6. Insert the JST VH terminals into the white JST VH housing. Use the two outermost slots.
# Emitter/Ballast Preparation
1. Place the emitter flat on a clean table, lens side down, with the green circuit board to your left.
2. Remove any screws from the “1” and “2” electrode terminals.
3. Connect the high voltage cable to the “1” and “2” electrode terminals.
  1. Use the two terminals closest to you.
  2. The high voltage cable should stick out towards you.
  3. Use the M2.5 x 8mm screws with captive lockwashers.
  4. Use a #1 phillips screwdriver, and torque the screws by hand to prevent damage.
4. Place the white emitter-ballast spacer on top of the emitter. The flat shield should cover the high voltage cables.
5. Screw the spacer in place with four black M2.5 flat head screws.
  1. Use a #1 phillips screwdriver, and the #3 torque setting on the Hitachi electric screwdriver.
6. Place the ballast on top of the spacer, with the CN101 high voltage connector closest to you.
7. Screw the ballast in place using four M3 self-tapping screws.
  1. Use a #1 phillips screwdriver, and the #3 torque setting on the Hitachi electric screwdriver.
8. Plug the high voltage cable onto connector CN101 of the ballast.
9. Connect the LED ignition cable.
  1. One end in CN102 of the ballast.
  2. The other end in CN1 of the emitter circuit board.
# Back Plate Preparation
1. Snap the fan into the housing back plate.
  1. Ensure the direction of airflow is inward.
  2. The wires should exit near the large flat surface of the back plate.
2. Insert the USHIO RP2040 Controller 1.0 power jack into the back place, ensuring the PCB is flush against the mounting pegs.
3. Screw the USHIO RP2040 Controller 1.0 in place using M3 self-tapping screws.
  1. Use a #1 phillips screwdriver, and the #3 torque setting on the Hitachi electric screwdriver.
4. Plug the radar PCB into the USHIO RP2040 Controller 1.0.
  1. Use a 5-pin jumper cable.
  2. Ensure the “TX” pin of the radar PCB matches up with the “TX” pin of the USHIO RP2040 Controller 1.0.
5. Plug the 4-pin JST XA cable into J2 of the USHIO RP2040 Controller 1.0.
# Housing Assembly
1. Place the housing flat on a clean table, emitter side down, with the fan grille facing you.
2. Lower the emitter-ballast assembly into the housing, with the high voltage cable facing you.
  1. The ballast PCB should be flush with the black plastic ledge of the housing.
  2. The high voltage cable should fit loosely, with black plastic of the housing on either side.
3. Place the radar PCB to the right side and slightly under the ballast PCB.
  1. Note, it will be secured in place by the back plate.
4. Plug in the 4-pin JST XA cable into CN100 of the ballast.
5. Carefully place the back plate onto the housing.
  1. This will require fiddling with the cables to ensure everything fits into place. Take your time, and beware of pinched cables.
6. Screw the back plate to the housing using four black M2.5 flat head screws.
  1. Use a #1 phillips screwdriver, and the #3 torque setting on the Hitachi electric screwdriver.
# Testing
1. Plug a 24V power supply into the power connector.
2. Turn on the cable’s power switch (if present).
3. Ensure the fan spins.
4. Ensure the UV lamp glows.